## Slide 1: Getting Started in VHF Roving
Bruce Richardson, W9FZ

## Slide 2
KK6MC/R in New Mexico

## Slide 3
Danny, N0SPN/R
Near Rochester, MN

## Slide 5: We have bands at:
50-54 MHz 6 Meters
144-148 MHz 2 Meters
222-225 MHz
420-450 MHz 70 cm
902-928 MHz
1240-1300 MHz
2300-2310 MHz
And higher

## Slide 6: Versatile Rigs – Do you own one?
Include 6 meters, 2 meters, and 70 cm !!

## Slide 7: Put the rig in the car
Front seat
Back Seat

## Slide 8: Put the rig in the car
Neat install!

## Slide 9: Put the rig in the car

## Slide 10: Operating: Rover
Hooking Up to DC Power
  DO NOT use the cigarette lighter!
  Run equipment to the car’s battery
  Consider adding a battery booster to maintain consistent 13.8 V output
  Car battery power will be just fine for the 50 to 100 watts the rig will put out

## Slide 11: Hook up to DC
No, don’t use the lighter
Run it to the battery
That will be just fine for the 50 and 100 watts the rig will put out
And 100 watts on 6m, 50w on 2 meters, and 50w on 432 MHz is just fine
Some integrate 2nd batteries into their systems

## Slide 12: Hook up to DC

## Slide 13: Coax
Low loss is best. Attenuation is db/ft
Hate to lose signal in lossy coax—both transmit and receive
Ultraflex is nice for rover installations

## Slide 14
My favorites are LMR-240UF for 6 Meters
and LMR-400UF for 2 Meters and 70cm
30 foot chunk

## Slide 16: Antennas
Omnis?
Range about 60 miles
Simple

## Slide 17: Operating: Rover
Simple Mag Mounts…

## Slide 18: Operating: Rover
“Tiny Tower”, Complete With Antenna Rotator…

## Slide 19
Beams – reach out and touch

## Slide 21: Commercial Beams
Cushcraft
M-Squared
Directive Systems
Beams: Increasing complexity to increase range and coverage

## Slide 22: WA5VJB “Cheap” Yagis
Kent designed an easily replicated antenna tolerant of abuse
http://www.wa5vjb.com/yagi-pdf/cheapyagi.pdf
Driven element is a “J”. Proximity of first director and reflector “load” the J such that feedpoint impedance is near 50 Ohms.
Build your own for minimal $

## Slide 31
432 MHz 222 MHz 144 MHz

## Slide 32: For 6 Meters
Dipole, Halo, or Moxon
I prefer a dipole
Height is VERY helpful
Hamstick if only working E-Skip ………..or if in a jam

## Slide 37
I work K2DRH, W9GA, W0UC, N9DG, and sometimes W0ZQ from hundreds of miles away using a dipole (on 6m) at 18
Feet (and CW).

## Slide 39
Short “sees” long
but long doesn’t “see” short

## Slide 42: Grid Corners are Nearby

## Slide 43: Grid Corners are Nearby

## Slide 44: Grid Corners are Nearby

## Slide 45: Grid Corners are Nearby

## Slide 46: Operating: Rover Sites
Choosing an operating site
  Topographic road maps
    Delorme state atlases
    especially useful
      Elevation contours
      Back roads, dirt roads, trails
  HeyWhatsThat.com
    Web-based terrain profile
    analysis
  Understand grid squares and grid corners

## Slide 47: How to pick spots
DeLorme map books are essential
RadioMobile software helps
Google Earth helps a little
Pre-scouting visits prove usefulness of site
You need a place big enough and safe enough to park – or possibly spin – the car

## Slide 52: Who are you going to work?
Fixed stations
And other
Rovers

## Slide 53: Logging
Simplest is paper
logging
Computer logging scores
and post-processes easily

## Slide 55
Rovers working other rovers repetitively over trivial distances around a grid intersection.
So What is Grid Circling?
It can lead to big scores and some
fun, but……….

## Slide 56
Yes!
What About FT-8 or FT-4?
This is N9SD who roves with his son. They do mostly FT-8
near Milwaukee
It is complex to integrate into a rover but other stations pull your signal out of the noise.

## Slide 57: Big Keys to Success
To be reliable to the fixed stations and make them come looking for you contest after contest:
Make a schedule and publish within the region
(Use W0UC’s google spreadsheet of activity as well as regional email reflectors)
Get off of 144.200!!! Pick a freq well away—that way fixed stations can hear you and work you easily
Stay on schedule
Ask for “Any other stations?” before jumping bands

## Slide 58: If you have one of those rigs
We NEED you to rove!!!!
It seems simple enough doesn’t it???
Might win “Limited Rover”—might not
You do not need to be a 7-band rover. We need you out there with 1, 2, or 3 bands having fun!
Please! Rove!

## Slide 59: Rover Talk Resources
This page is at: https://w9fz.com/rovertalkresources.html
Facebook “Ham Radio Rovers” Group: https://www.facebook.com/groups/1000514463430244
Northern Lights Radio Society local VHF email reflector: https://nlrs.club/#Email%20Reflector
EXAMPLE of W0UC’s Upper Midwest Contact Activity spreadsheet with tabs for Fixed stations and Rovers: https://tinyurl.com/VHFss2022 (example only of a past event—each new event is announcd on the NLRS email reflector)
Notable Rovers on QRZ.com K2EZ https://www.qrz.com/db/K2EZ N0LD https://www.qrz.com/db/N0LD
Central States VHF Society is having their annual conference in La Crosse, WI on July 22nd and July 23rd. Website is not up (yet) for it but the weblink will be https://2022.csvhfs.org . In addition to all the technical talks and socializing, there is “Rover Row” on Friday morning from 8am to Noon where many rovers give “shack tours” of their rovers. Lot’s of good ideas shared.
And this PowerPoint will be at: https://w9fz.com/ham/MGRC_RoverTalk22.pptx